## Slide 1
ci-scripts: Shared CI scripts for EPICS modules

## Slide 2
What?
EPICS module helper scripts for CI services as a Git submodule
Easy to use:
  Add ci-scripts as a Git submodule to your EPICS software module
  Copy an example configuration and adapt it to your needs
  Activate your repository on the CI service platform
Features:
  Compile against different branches or releases of EPICS Base and additional dependencies (modules like asyn, std, sequencer, etc.)
  Define setup files with sets of dependencies (versions and locations)
  Cross-compile to RTEMS, running tests in the qemu emulator
  Git submodule: developments in ci-scripts can’t break your module
Supports multiple free public CI services

## Slide 3
Supported CI Services
Travis-CI (https://travis-ci.org/)
  Five runners on Linux/Windows (one on MacOS)
  Host builds on Linux (gcc, clang), MacOS (clang) and Windows (gcc/MinGW, VS 2017)
  Cross builds for RTEMS 4.9 & 4.10, Windows (MinGW/WINE)
  Dependencies are cached (faster builds)
AppVeyor (https://ci.appveyor.com/)
  Only one runner (all builds are sequential)
  Host builds on Windows Server (2012/2016/2019)
  Compilers: gcc/MinGW, VS 2008, 2010, 2012, 2013, 2015, 2017, 2019
  32bit or 64bit, DLL or static, debug or optimized
  No useful caching available

## Slide 4
Supported CI Services
GitHub Actions (https://github.com/)
  20 runners on Linux/Windows (5 on MacOS)
  Ubuntu 16/18/20, MacOS 10.15, Windows Server 2016/2019
  Host builds on Linux (gcc, clang), MacOS (clang) and Windows (gcc/MinGW, VS 2017 & 2019)
  Cross builds for RTEMS 4.9 & 4.10, Windows (MinGW/WINE)
  Caching not supported yet
GitLab CI/CD (https://gitlab.com/)
  Docker-based runners on Linux (one VM per job)
  Can use any Docker image from Dockerhub
  Example uses ubuntu:bionic, compiling with gcc/clang
  Cross builds for RTEMS 4.9 & 4.10, Windows (MinGW/WINE)
  Dependencies are cached (faster builds)

## Slide 5
Status and Roadmap
Current users:
EPICS Base and its submodules pvData, pvAccess, pva2pva, PVXS
EPICS Modules: ASYN, autosave, busy, devlib2, ecmc, gtest, ip, lua, MCoreUtils, modbus, motor, mrfioc2, OPC UA, PCAS, softGlueZync, sscan, std, vac, xxx
ESS: EtherCAT MC Motor Driver
https://github.com/epics-base/ci-scripts
Cross-builds for RTEMS 5 are next